## Slide 1
USS John Finn (DDG 113)
UNCLASSIFIED – FOR OFFICIAL USE ONLY (FOUO)
____________________ ____________________ ____________________
NAV XO CO
      NAVIGATION BRIEF
      PEARL HARBOR, HI OUTBOUND
      25 MAR 2021

## Slide 2: USS John Finn (DDG 113) REFERENCES
UNCLASSIFIED
CNSL/CNSP/CNAL/CNAP 3530.4F NAVDORM
JOHNFINNINST 3121.1D
Coast Pilot 7, Chapters 2 & 4
PUB 941 Pearl Harbor Fleet Guide
Navigator

## Slide 3: USS John Finn (DDG 113) WATCHBILL
UNCLASSIFIED
Navigator
CIC | 
CICWO | LTJG Valencia ENS Giannotti (U/I)
Shipping Officer | OS1 Ronsse
Piloting Officer | OS2 Harris
BRIDGE | 
OOD | LTJG Gormley ENS Lutton (U/I)
JOOD | ENS Conkey
JOOW | LTJG Bilden
CONN | ENS Peterson
NAV Evaluator | LTJG Lowery
VMS Operator | QMC Heindl
Helm Safety Officer | ENS Byrom
Master Helmsman | RS3 Howard
Lee Helmsman | BMSN Williams
Shipping Liaison | OS2 Barry
CCS | 
PCO | LT Chillmen
EOOW | GSCS Lapid
PACC | GSM2 Martorano
EPCC | EM2 Campano
RSC | DC2 Audette

## Slide 4: USS John Finn (DDG 113) TIMELINE
UNCLASSIFIED
Timeline
  Station sea and anchor detail:
  Underway
  IVO of 2 NM from land/shoal:
Consideration of options Time Zone: +10W
  Tides: High
  Currents: No current station: not usually strong;
              however, a westerly set is normally present.
              Arriving at slack water.
  Speed restrictions: 10 kts after Light #7;
      6 kts speed restriction around shipyard and berthing pier areas (NE of light 20);
      No wake zone IVO USS ARIZONA Memorial
Operation requirements
  Condition of readiness: COND III
  Tactical situation: N/A
Navigator
1400
1500
1600

## Slide 5: USS John Finn (DDG 113) WEATHER
UNCLASSIFIED
Navigator
Notes: https://marine.weather.gov/MapClick.php?w0=t&w1=td&w2=hi&w3=sfcwind&w3u=0&w4=sky&w5=pop&w6=rh&w7=rain&AheadHour=40&Submit=Submit&FcstType=graphical&textField1=21.1957&textField2=-158&site=all&unit=0&dd=&bw=&marine=1

## Slide 6: USS John Finn (DDG 113) TIDES
UNCLASSIFIED
Navigator
TIDE
FORD ISLAND FERRY DOCK
TIDE
BISHOP POINT

## Slide 7: USS John Finn (DDG 113) TIDES
UNCLASSIFIED
Pearl Harbor, Ford Island Ferry
Navigator
1515 +0.65 ft MLLW
Notes: https://tidesandcurrents.noaa.gov/tide_predictions.html?gid=1399

## Slide 8: USS John Finn (DDG 113) TIDES
UNCLASSIFIED
Pearl Harbor Entrance, Bishop Point
Navigator
1530 +0.65 ft MLLW
Notes: https://tidesandcurrents.noaa.gov/tide_predictions.html?gid=1399

## Slide 9: USS John Finn (DDG 113) ASTRONOMICAL DATA
UNCLASSIFIED
Sunrise:
Sunset:
Moonrise:
Moonset:
Moon Phase: Waxing Gibbous
Lunar Illumination: 94%
Navigator
0630
1845
1603
0519
Notes: Admiralty Total Tides

## Slide 10: USS John Finn (DDG 113) NAVIGATION DATA
UNCLASSIFIED
VMS | 
DNC | 13
LNTM | 12 / 21
NTM | 12 / 21
HYDROPAC | 904/2021
NAVAREA XII | 124/2021
Shoal Water | 36ft (black in VMS)
GPS Datum | WGS 84
Charts | H1356280 A1356285 COA13C GEN13C
LOCAL INFO | 
Buoyage System | IALA B (red, right, returning)
Line of Demarcation | Line from Barber’s Point Light to Diamond Head Light
VTS | None
Degaussing | Range IVO Waipio Point Monitor BTB CH 74
Navigator
NAVIGATION MESSAGES | 
NAVCERT MSG DTG | 042035ZOCT16 082100ZJUN17 031935ZAUG18

## Slide 11: USS John Finn (DDG 113) NAVIGATION DATA
UNCLASSIFIED
Navigator
PIER INFORMATION | 
PIER | M1
BERTH | 1 PST
PIER HDG | 154°T / 144°M
MAG. VAR | 10°E
SURF. WINDS | SW 6KTS
INT’L CALL SIGN (NJFN) | Closed up pier side Hauled down LOD
BATTLE FLAG (MEDIUM SIZE) | Closed up pier side
SW 6 KTS

## Slide 12: USS John Finn (DDG 113) SPECIAL CONSIDERATIONS
UNCLASSIFIED
Honors: IAW NTP 13(B)
Flag Officer movements: N/A
Visitors: N/A
Harbor exercises: N/A
Debrief: In the pilothouse once S&A detail is secured
Uniform: FRVs with command ball caps
Navigator

## Slide 13: USS John Finn (DDG 113) TRACK
UNCLASSIFIED
Danger bearings/ranges: N/A
Shoal: Marked in BLACK, danger sounding of 36 ft
Channel depth:
Channel width:
Conning Officer
LOCATION | LEFT OUTSIDE QUARTER | MIDDLE HALF | RIGHT OUTSIDE QUARTER
Outer entrance channel (up to Beacon 5) | 48.8 ft | 48.8 ft | 59.8 ft
Entrance channel (NAV beacon 5-19) | 41.9 ft | 41.9 ft | 41.1 ft
Main channel | 43.8 ft | 43.8 ft | 43.8 ft
South channel | 36.6 ft (Shallowest) |  | 
Turning basin | 41.4 ft (Shallowest) |  | 
LOCATION | WIDTH
Outer entrance channel | 100 yds
Entrance channel | 100-251 yds
Main channel | 158 yds
South channel | 282 yds
Turning basin | 380 yds
Notes: Fleet guide reports South CH and turning basin dredged to 45 feet (MMLW)

## Slide 14: USS John Finn (DDG 113) TRACK DATA SHEET
UNCLASSIFIED
Conning Officer
* ALL TURNS BASED ON A STANDARD RUDDER*7 |  |  |  |  | 
LEG | COURSE | DISTANCE | SPEED | TB | TR
1 | 245T /235M | 625 YDS | 6 | N/A | N/A
2 | 246T / 236M | 849 YDS | 6 | JW 165T / 262R | R15 509 YDS
3 | 183T / 173M | 2,442YDS | 10 | TIKI 233T / 056R | R6 698 YDS
4 | 168T/ 158M | 1,598YDS | 10 | POKE 048T / 250R | R3 742 YDS
5 | 154°T/144°M | 7,140 YDS | 15 | N/A | N/A
6 | 180°T/170°M | 10,980 YDS | 15 | N/A | N/A
Notes: TB – COURSE = R DECIMAL x 2K = YDS

## Slide 15: USS John Finn (DDG 113) TRACK
2
C- 246°T / 236°M
S- 6 KTS
D- 849 YDS
Conning Officer
USS ARIZONA MEMORIAL: NO WAKE ZONE
PIER M1
R15
1
C- 245°T / 235°M
S- 6 KTS
D- 625YDS
TB1 JW: 165T / 262R
T1 R15: 509YDS

## Slide 16
USS John Finn (DDG 113) TRACK
Conning Officer
4
C- 168°T / 158°M
S- 10 KTS
D- 1,598 YDS
3
C- 183°T/173°M
S- 10 KTS
D- 2,442 YDS
TB2 TIKI: 233T / 065R
TB3 P: 048T / 250R
TR2 R6: 698 YDS
TR3 R3: 742 YDS
PILOT DROP OFF
T
P
R6

## Slide 17
USS John Finn (DDG 113) TRACK
Conning Officer
5
C- 154°T / 144°M
S- 15 KTS
D- 7.140 YDS
“PH”
Line of Demarcation
Holokahiki Pt Church
TB1 DIAMOND HEAD: 088.5°T / 088.5°R
TB2 HOLOKAHIKI POINT: 068.4°T / 042.4°R
TR1 AIRFIELD: 6,420 YDS
TR2 BISHOP POINT: 1,541YDS
BUOY 1
Speed Restricted 10 kts
UNCLASSIFIED
6
C- 180°T / 170°M
S- 15 KTS
D- 10,980 YDS
6
C- 180°T / 170°M
S- 15 KTS
D- 11,260 NM

## Slide 18: USS John Finn (DDG 113) GROUND TACKLE
UNCLASSIFIED
Ready anchor: Centerline
Scope of chain: 5 times depth of water
Method of letting go/weighing anchor: From the brake
EQUIP | STATUS
FWD Capstan | 
AFT Capstan | 
Windlass | 
Accommodation Ladder | (STOWED)
1217 IRISH GUNNER | (RLB)
1218 HAWAIIAN WARRIOR | 
1st LT

## Slide 19: USS John Finn (DDG 113) MOORING CONFIGURATION
UNCLASSIFIED
Pier M1
1st LT

## Slide 20: USS John Finn (DDG 113) OPERATIONAL CONSIDERATIONS
UNCLASSIFIED
Harbor special event: NONE
Media coverage: Not Anticipated
Flight ops (FOD/VERTREP PAX transfer): N/A
Hot areas: N/A
HARBOR MOVEMENTS
OPS
TIME | UNIT | FROM | TO
0900 | SYDENY | SEA | H2
1530 | USS Chicago | S-11 | SEA

## Slide 21: USS John Finn (DDG 113) TUG AND PILOTS
UNCLASSIFIED
Tug and Pilot: 1 pilot CAPT Stark, Tiger 1 and 3
Pick up: Pierside
Drop off: IVO Hospital Point
Comms: BTB CH 16, 69
INTERNAL COMMUNICATIONS |  | 
STATION | PRIMARY | SECONDARY
NAVIGATION | NET 22 | X1JV
LOOKOUT | NET 52 | X27J
STEERING | NET 53 | X40J
DECK | NET 56 | SWICS B09
CO BATTLE NET | NET 15 | NET 16
GUARD STATIONS | 
NAVY RED | CIC
FLT TAC | CIC
BTB | BRIDGE
Navigator

## Slide 22: USS John Finn (DDG 113) COVID-19 Considerations
UNCLASSIFIED
Navigator
Requirements
  Clean and sanitize bridge one hour prior to arrival
  Essential personnel on the bridge only
  Hand sanitizer available on the bridge
  No handshakes
  Adhere to physical distancing
  All personnel will be wearing masks

## Slide 23
USS John Finn (DDG 113) STATUS OF NAVIGATION EQUIPMENT
UNCLASSIFIED
QMOW
RADAR ERROR |  | 
RADAR | BEARING ERROR | RANGE ERROR
SPS-67 (25MAR) | 0.5°E | 21 YDS LNG
BME (25MAR) | 0.5°E | 62 YDS LNG
GYRO/REPEATER STATUS (25MAR) |  | 
GYRO ERROR: 0.1°E | REPEATER ERROR | TOTAL ERROR
METHOD: Azimuth |  | 
Centerline Pelorus | 0.0° | 0.1°E
SCC | 0.1°E | 0.2°E
PORT | 0.3°E | 0.4°E
STBD | 0.1°E | 0.2°E
Aft Steering | 0.2°W | 0.1° W

## Slide 24: USS John Finn (DDG 113) STATUS OF NAVIGATION EQUIPMENT
NAV EQUIPMENT |  |  | 
EQUIP | STATUS | EQUIP | STATUS
FWD WSN-7 |  | Fathometer | 
AFT WSN-7 |  | VHF (BTB) | 
DEML |  | Ship’s Whistle | 
GPS 1 |  | NAV Lights | 
GPS 2 |  | AIS | 
RTS 1 |  | MORIAH | 
RTS 2 |  | STBD MFCR | 
SPS-67 |  | PORT MFCR | 
BME |  | SPA-25 (Bridge) | 
DFGMC |  | SPA-25 (CIC) | 
UNCLASSIFIED
ECDIS-N | 
EQUIP | STATUS
NAV 1 | 
NAV 2 | 
NAV 3 | 
CONN 1 | 
CONN 2 | 
HFS | 
BCCS | 
CO LAPTOP | 
SPCS | 
ENL | 
EQUIP | STATUS
ENL | 
DAGR | 
Navigator

## Slide 25: USS John Finn (DDG 113) STATUS OF ENGINEERING PLANT
UNCLASSIFIED
POWER/PROPULSION |  | 
GTM |  | CONDITION
1A |  | Online
1B |  | Online
2A |  | Online
2B |  | Online
GTG |  | CONDITION
1 |  | Online
2 |  | Running Offline
3 |  | Online
Thrust Control: SCC Lee Helm |  | 
Auxiliary Control: UCC1 |  | 
RMD: Pierside |  | 
STEERING |  | 
HPU |  | CONDITION
1A |  | Online
1B |  | Running Offline
2A |  | Online
2B |  | Running Offline
Steering Control: SCC Helm |  | 
Computer Manual |  | 
MISC | 
Degaussing | ON
Limiting Casualties | N/A
PCO
Notes: NAVDORM delineates “Engineer Officer (or Reactor Officer/Plant Control Officer)” specifically, not the EOOW.

## Slide 26: USS John Finn (DDG 113) RMD
UNCLASSIFIED
PCO
Maximum plant reliability will be set prior to setting RMD
Specific deviations from EOCC that may not be conducted without CO permission:
  Do not take thrust or pitch control from the Bridge
  Do not secure the last engine on each shaft
  For shafting casualties, do not stop either shaft
  Do not go to single generator operations
  Do not electrically isolate any switchboard
  Do not perform any planned/corrective maintenance or authorize new tag outs

## Slide 27
USS John Finn (DDG 113) LOSS OF STEERING
UNCLASSIFIED
Master Helmsman
Report to CONN, “Loss of steering control”
Depress EMERGENCY OVERRIDE TO MANUAL pushbutton; verify BACKUP MANUAL is displayed on the SCC
Verify power unit RUN and RUDDER ENGAGE indicators are illuminated for both rudders
Test for rudder control; report to CONN
Shift to standby power units
  Select the standby pumps Engage buttons
  Select the online pumps STOP buttons
  Verify Port/Stbd Run and Engage indicators illuminate for standby units and extinguish for online units
  Test for rudder control; report to CONN
Shift to after steering
Notes: OOD to brief verbally loss of steering

## Slide 28: USS John Finn (DDG 113) LOSS OF STEERING
UNCLASSIFIED
AFT Steering Helm
Shift to after steering
  Depress EMERGENCY OVERRIDE TO MANUAL pushbutton; verify AFT is displayed as steering control location
  Test for rudder control; report to CONN via net 53
  If steering is regained, CONN will issue a new order via net 53
Shift to LCUs
  Turn engaged HPU LCU HELM CONTROL switched to LOCAL
  Test for rudder control; report to CONN via net 53
  If required, engage standby power units
  Turn engaged HPU LCU HELM CONTROL switched to LOCAL
  Test for rudder control; report to CONN via net 53
  If steering is regained, CONN is limited to giving rudder orders only
  NOTE: If steering control is not regained at the LCU, operational steering is not possible.
Shift to Fill and Drain Pump
Shift to Manual Hand Steering Pump
Shift to Ratchets
Notes: OOD to brief verbally loss of steering

## Slide 29
USS John Finn (DDG 113) LOSS OF THRUST CONTROL
UNCLASSIFIED
LEE HELMSMAN
Report to CONN, “Loss of thrust control”
CCS will take thrust control from the pilothouse IAW MLTC
CCS will than test for positive thrust control by +/- 2 shaft RPM or +/- 2% pitch and report to the JOOD via net 53

## Slide 30: USS John Finn (DDG 113) EMERGENCIES
UNCLASSIFIED
OOD
Loss of Steering:
  Pass the word on the 1MC
  Ensure positive communications with after steering via net 53
  Slow to safe speed
  Make PAN PAN call over BTB to inform ships in the vicinity
  Hoist ball over ball, energize red over red
  If steering control is not regained at the LCU, CONN will attempt to steer ship using various RPM and PITCH combinations
Man Overboard:
  Drop smoke float and life ring
  Sound six short blasts of the ship’s whistle
  Pass the word on the 1MC, ship riders will muster on messdecks
  Make PAN PAN call over BTB to notify ships in vicinity
  Hoist OSCAR, energize red over red pulsating lights
  Primary means of recovery will be tugs or harbor security boats
  Medical will be standing by on recovery station to assist
Notes: OOD to brief verbally loss of steering

## Slide 31: USS John Finn (DDG 113) EMERGENCIES
UNCLASSIFIED
OOD
Loss of Gyro:
  Shift to secondary gyro
  If gyro is not restored, shift to DFGMC
  Navigation will shift to a relative plot
  NOTE: If loss of steering occurs while JFN has a loss of gyro, CONN will drive with rudder in hand.
Loss of VMS Display:
  Shift to alternate VMS display on the bridge
Loss of primary position source (GPS 1):
  Shift to GPS 2
  Shift to DAGR
  Shift to Visual/radar/composite
  Shift to COTS GPS
Loss of RADAR:
  Upon loss of SPS-67, shift to BME, then steer by seaman's eye.

## Slide 32: USS John Finn (DDG 113) EMERGENCIES
UNCLASSIFIED
OOD
Loss of external communications:
  Shift to handheld BTB radios. Upon loss of handheld BTB, shift to signal flags.
Reduced visibility:
  JOOD complete low visibility checklist
  Station the low visibility detail
  Slow to safe speed
  Energize navigation lights
  Sound fog signals IAW NAVIGATION RULES
Emergency anchorage locations:
  Restricted to the channel until buoys 1 & 2
  IVO Waipio Point slightly east of the channel
  IVO South Channel and Turning Basin
  Caution must be exercised to avoid cables and pipeline crossings

## Slide 33: USS John Finn (DDG 113) EMERGENCIES
UNCLASSIFIED
EOOW
Propulsion Casualties:
  Throttle control will remain in the Pilothouse at the Ship’s Control Console (SCC).
  If there is a loss of display/control, thrust will shift to the MCS PACC Console.
  Test for propulsion control by +/- 2 shaft RPMs or 2 percent pitch.
  Battle Override will be activated on last GTM on each shaft. The CO will be notified immediately when Battle Override is activated.
CRP Casualties:
  The affected OD box operator will take local manual control of pitch and answer “percent pitch” commands as directed by the helm safety officer on net 53
  Testing of pitch control will be of no more than +/- 2 percent.
Electrical Plant Casualties:
  If possible, EOOW parallel the standby generator with the properly functioning GTG prior to opening the GTG breaker of the affected GTG. EPCC actions shall be such that ZEDS is not interrupted.
  In the case of a loss of generator, follow normal EOCC but DO NOT RE-ENERGIZE a dead bus.
  In the event of a loss of two generators, the EPCC will manually initiate stage two load shed in order to maintain propulsion and steering.

## Slide 34: USS John Finn (DDG 113) FORCE PROTECTION PLAN
UNCLASSIFIED
c
252
251
502
501
507
508
GLO
SCAT status: (4) .50 cals, (2) ROCs will be manned
Small boat escort: N/A
PPRs: IAW JOHNFINNINST 3300.1B
COMMS plan: Primary – SIWCS 9B
          Secondary – NET 68
c
c

## Slide 35: USS John Finn (DDG 113) RISK ASSESSMENT/ORM
UNCLASSIFIED
Navigator
HAZARD | ASSESS | RAC | CONTROL | ASSESS | RRAC | SUPERVISOR
Collision | D/I | 2 | Utilize BTB early, build SA by monitoring current ship movements, shipping officer on station, make course changes early, maneuver IAW the ROTR and sound danger signal as necessary, AIS in transmit | E/I | 3 | OOD, NAV, XO, CO
Allision | D/I | 2 | Channel is well marked, safeties on fo’c’sle and flight deck passing ranges to the pier and watching for buoys. | E/I | 3 | DECK SAFETIES, NAV, XO, CO
Grounding | D/I | 2 | Shoal water marked in black, NAV reports as required, verbal fathometer readings | E/I | 3 | SONAR, NAV, XO, CO
NAV Equip. Malfunction | C/II | 2 | Casualty control procedures in place, redundant systems in place pre underway checks complete, NAV ET on station | D/II | 3 | NAV ET, NAV, XO, CO

## Slide 36: USS John Finn (DDG 113) RISK ASSESSMENT/ORM
UNCLASSIFIED
Navigator
HAZARD | ASSESS | RAC | CONTROL | ASSESS | RAC | SUPERVISOR
Comms Failure | C/II | 2 | Redundant systems in place, secondary comms identified and briefed pre-underway checks complete | D/II | 3 | CICWO, OOD
Breakdown in BRM | C/III | 3 | Briefed NAV plan, charts up to date, charts reviewed and approved, qualified personnel on station, forceful backup | D/III | 4 | CONN, JOOD, OOD, NAV, XO, CO
Distraction/ Fatigue | C/II | 2 | Supervisors keep watchstanders focused on the mission, emphasize safety is paramount, maintain quiet on station | D/II | 3 | CICWO, OOD, NAV, XO, CO
Unfamiliar port | B/II | 3 | Watchteam briefed and reminded to keep priorities in check. Charts and plan reviewed and approved. | C/II | 3 | NAV, OOD, XO, CO

## Slide 37: USS John Finn (DDG 113) RISK ASSESSMENT/ORM
UNCLASSIFIED
Navigator
HAZARD | ASSESS | RAC | CONTROL | ASSESS | RRAC | SUPERVISOR
Man Overboard | D/I | 2 | Utilize RHIB, tugs if available, ensure lifelines are properly rigged, safety brief conducted, safety observers and HM on station | E/I | 3 | DECK SAFETIES
Line Handling Mishap | D/I | 2 | Safety brief conducted, safety observers and HM on station, enforcing proper PPE | E/I | 3 | DECK SAFETIES
Steering/ Propulsion Casualty | D/I | 2 | Casualty control procedures in place, redundant systems in place, steering checks conducted, loss of steering and loss of thrust procedures reviewed on station when S&A is set, RMD/Max Plant Reliability set | E/I | 3 | MASTER HELM, HELM SAFETIES, EOOW, CONN, OOD
Inclement Weather | D/II | 3 | Maintain a proper lookout & safe speed at all times, muster low visibility detail in conjunction with S&A detail | E/II | 4 | CICWO, CONN, OOD, NAV, XO, CO
COVID-19 | D/II | 3 | Ensure sanitizer and wipes are on station. Ensure all personnel are wearing masks and maintaining social distancing. | E/II | 4 | OOD, CONN, JOOD, NAV, XO, CO, PILOT ESCORT

## Slide 38: USS John Finn (DDG 113) RISK ASSESSMENT/ORM
UNCLASSIFIED
Navigator

## Slide 39: USS John Finn (DDG 113) INDIVIDUAL RISK MANAGEMENT
UNCLASSIFIED
WATCHSTATION | WATCH/ REST RATIO | EXPERIENCE | CREW COHERENCE | EQUIPMENT | IRM
OOD: LTJG GORMLEY | 3 | 2 | 4 | 3 | 12
JOOD: ENS CONKEY | 3 | 2 | 4 | 3 | 12
JOOW: LTJG BILDEN | 3 | 2 | 4 | 4 | 13
CONN: ENS PETERSON | 3 | 2 | 4 | 3 | 12
MASTER HELM: RS3 HOWARD | 3 | 2 | 4 | 3 | 12
LEE HELM: BMSN WILLIAMS | 3 | 2 | 4 | 3 | 12
HELM SAFETY: ENS BYROM | 3 | 2 | 4 | 3 | 12
NAV EVAL: LTJG LOWERY | 3 | 3 | 4 | 4 | 14
CICWO: LTJG VALENCIA | 3 | 2 | 4 | 4 | 13
EOOW: GSCS LAPID | 3 | 2 | 4 | 4 | 13
XO: CDR GONZALES | 3 | 3 | 3 | 4 | 13
CO: CDR CATHEY | 3 | 3 | 4 | 4 | 14
OVERALL | 3 | 2.25 | 3.9 | 3.5 | AVE: 12.7
Navigator
Watch to Rest Ratio:
4: Watch leading into event (or during scheduled watch), 7 hours of sleep in last 24 hours
3: 7 hours of sleep in last 24 hours, stood a full watch before event
2: Between 5 and 7 hours of sleep in last 24 hours
1: Less than 5 hours of sleep in last 24 hours
Experience:
4: 11 or more similar evolutions in last 3 months
3: 5-10 similar evolutions in last 3 months
2: 5 or less similar evolutions in last 3 months; or U/I
1: First time as qualified watchstander
Equipment:
4: All equipment operational
3: Slight degradation
2: Moderate degradation
1: Primary / backup equipment OOC
IRM:
<8: Critical
8-10: Serious
11-13: Moderate
13-14: Minor
>14: Negligible
Crew Coherence:
4: Permanently Assigned Crew
3: Permanently Assigned Crew/TEMADD >6 Months
2: Permanently Assigned Crew/TEMADD between 3-6 Months
1: Permanently Assigned Crew/TEMADD/Cross deck <3 Months

## Slide 40: USS John Finn (DDG 113) LESSONS LEARNED
UNCLASSIFIED
Navigator
NSTR

## Slide 41: USS John Finn (DDG 113) QUESTIONS?
UNCLASSIFIED
QUESTIONS?